## Slide 1: ImageJ/FIJI image processing basics
Dr. Dominic Alibhai & Dr. Stephen Cross
Download “ExampleData.lif” from https://goo.gl/YrBvRU
Start Fiji (Start > All Programs > Fiji)

## Slide 2: Overview
Brief Introduction to image acquisition and basic image processing techniques
Hands on image processing with Fiji/ImageJ
  Step by step guide to different image processing concepts in Fiji
  Exercises for you to complete on each section
Useful Websites for further reading:
  https://www.microscopyu.com/
  https://svi.nl/AboutMicroscopy
  http://zeiss-campus.magnet.fsu.edu/tutorials/
  http://www.leica-microsystems.com/science-lab/
  https://imagej.nih.gov/ij/docs/guide/user-guide.pdf

## Slide 3: Overview
Raw data + pre-processing
Image processing + segmentation
Object identification
Quantification

## Slide 4
Acquisition
Visualisation
Segmentation
Quantification
Sample prep
Experimental Steps
Notes: Good analysis requires good samples acquired properly
Crap in  crap out

## Slide 5
Resolution is the minimum distance between two points which allows them to be distinguished as individual objects
It is the NA of the objective which determines the resolution - not the magnification
D
F
θ
Objectives, Numerical Aperture and Resolution
Notes: In Camera Systems need to balance mag with NA as fixed camera pixel size to get best resolution

## Slide 6
Correction | Magnification | Numerical Aperture | F(trans) | F(epi)
Plan Achromat | 10x | 0.25 | 6.25 | 0.39
Plan Apo | 10x | 0.45 | 20.2 | 4.10
Plan Fluorite | 20x | 0.50 | 6.25 | 1.56
Plan Apo | 20x | 0.75 | 14.0 | 7.90
Plan Achromat | 40x | 0.65 | 2.64 | 1.11
Plan Apo | 40x (oil) | 1.30 | 11.0 | 18.0
Plan Fluorite | 60x | 0.85 | 2.01 | 1.45
Plan Apo | 60x (oil) | 1.40 | 5.4 | 10.6
Plan Apo | 100x (oil) | 1.40 | 1.96 | 3.84
Plan Apo | 100x (oil) | 1.45 | 2.10 | 4.42
For a given NA, lower magnification gives a brighter image
Magnification and image brightness
Notes: Camera systems -> need to balance light throughput with pixel size

## Slide 7: Bit Depth and digital images
20 | 24 | 31 | 38 | 39 | 43 | 40 | 39 | 41 | 39 | 45 | 44 | 43 | 40 | 35 | 26 | 23 | 21 | 16 | 15 | 12 | 15 | 10 | 9
24 | 27 | 31 | 33 | 39 | 36 | 41 | 38 | 39 | 40 | 42 | 45 | 43 | 44 | 34 | 29 | 27 | 22 | 17 | 14 | 13 | 11 | 8 | 10
25 | 25 | 31 | 37 | 41 | 41 | 41 | 41 | 37 | 36 | 36 | 45 | 43 | 40 | 39 | 33 | 27 | 23 | 15 | 16 | 15 | 13 | 12 | 13
20 | 25 | 24 | 36 | 39 | 38 | 41 | 37 | 39 | 39 | 38 | 39 | 43 | 37 | 39 | 35 | 30 | 24 | 20 | 19 | 12 | 14 | 13 | 11
24 | 25 | 29 | 36 | 35 | 39 | 37 | 39 | 38 | 37 | 38 | 42 | 41 | 42 | 42 | 38 | 37 | 27 | 26 | 23 | 19 | 17 | 17 | 15
27 | 24 | 32 | 38 | 37 | 42 | 37 | 39 | 41 | 41 | 35 | 41 | 38 | 48 | 42 | 40 | 36 | 31 | 29 | 26 | 20 | 20 | 17 | 19
26 | 25 | 31 | 32 | 32 | 38 | 40 | 37 | 38 | 35 | 40 | 39 | 40 | 46 | 40 | 39 | 38 | 41 | 35 | 28 | 27 | 24 | 19 | 20
27 | 22 | 32 | 35 | 38 | 34 | 38 | 40 | 37 | 39 | 40 | 41 | 37 | 37 | 38 | 43 | 43 | 41 | 38 | 36 | 31 | 30 | 27 | 25
24 | 30 | 30 | 40 | 40 | 40 | 39 | 36 | 41 | 34 | 39 | 40 | 40 | 40 | 41 | 42 | 42 | 44 | 42 | 42 | 37 | 36 | 33 | 37
28 | 34 | 37 | 41 | 41 | 40 | 43 | 38 | 41 | 42 | 40 | 37 | 35 | 35 | 40 | 37 | 39 | 41 | 42 | 41 | 42 | 42 | 40 | 40
31 | 35 | 41 | 40 | 42 | 44 | 45 | 46 | 43 | 37 | 42 | 39 | 36 | 39 | 39 | 38 | 41 | 39 | 40 | 38 | 45 | 42 | 42 | 41
34 | 38 | 40 | 42 | 41 | 44 | 44 | 48 | 47 | 41 | 43 | 38 | 39 | 39 | 37 | 39 | 39 | 39 | 39 | 37 | 42 | 44 | 40 | 39
38 | 41 | 41 | 47 | 46 | 49 | 46 | 44 | 47 | 42 | 39 | 41 | 36 | 39 | 36 | 38 | 36 | 35 | 39 | 37 | 37 | 39 | 42 | 41
42 | 48 | 47 | 45 | 50 | 49 | 46 | 46 | 46 | 50 | 48 | 47 | 40 | 35 | 36 | 40 | 37 | 39 | 36 | 40 | 37 | 36 | 37 | 41
44 | 45 | 54 | 52 | 54 | 48 | 50 | 45 | 47 | 44 | 47 | 43 | 50 | 41 | 41 | 36 | 38 | 36 | 41 | 39 | 37 | 37 | 37 | 37
44 | 47 | 47 | 55 | 49 | 50 | 48 | 51 | 46 | 44 | 44 | 45 | 47 | 45 | 40 | 43 | 36 | 40 | 36 | 36 | 36 | 32 | 37 | 39
43 | 46 | 50 | 51 | 54 | 52 | 50 | 48 | 47 | 47 | 51 | 46 | 42 | 41 | 42 | 41 | 41 | 39 | 38 | 38 | 38 | 39 | 38 | 40
45 | 50 | 50 | 47 | 43 | 48 | 44 | 45 | 50 | 45 | 45 | 44 | 48 | 44 | 43 | 43 | 43 | 40 | 41 | 34 | 35 | 38 | 40 | 38
46 | 45 | 43 | 42 | 34 | 38 | 36 | 41 | 42 | 43 | 44 | 43 | 42 | 44 | 51 | 48 | 43 | 41 | 41 | 38 | 36 | 39 | 35 | 39
41 | 39 | 39 | 35 | 35 | 29 | 29 | 32 | 33 | 36 | 39 | 37 | 44 | 43 | 46 | 43 | 43 | 43 | 39 | 40 | 39 | 39 | 41 | 39
38 | 30 | 34 | 29 | 28 | 29 | 27 | 26 | 28 | 32 | 33 | 38 | 42 | 42 | 44 | 44 | 45 | 48 | 39 | 43 | 40 | 45 | 39 | 43
29 | 30 | 29 | 24 | 24 | 23 | 27 | 29 | 25 | 28 | 30 | 38 | 33 | 40 | 43 | 43 | 46 | 44 | 46 | 46 | 42 | 42 | 46 | 42
26 | 24 | 25 | 23 | 22 | 21 | 26 | 25 | 23 | 28 | 28 | 29 | 35 | 41 | 39 | 42 | 41 | 43 | 48 | 48 | 44 | 45 | 46 | 40
25 | 24 | 22 | 22 | 20 | 22 | 17 | 19 | 23 | 23 | 25 | 27 | 32 | 36 | 40 | 41 | 49 | 46 | 40 | 48 | 47 | 43 | 48 | 44
1 bit | 21 | 2
8 bit | 28 | 256
12 bit | 212 | 4096
16 bit | 216 | 65536

## Slide 8
Oversampled
Not ‘bad’ but will take longer and cause more photodamage to the sample
Sampling an image
Nyquist sampled
Minimum sampling rate to capture the signal
Under sampled
Aliasing
Notes: Sampling of image just like sampling other things e.g. converting music from analogue to digital

## Slide 9: Sampling an image
Smaller features in image correspond to higher spatial frequencies
When setting pixel size (in confocal), important to sample image appropriately to avoid aliasing in image.
Rule of Thumb:
Not always possible due to photobleaching etc.
Need to be aware of roughly the smallest feature you are interested in.
http://svi.nl/NyquistRate - lots of information on Nyquist sampling + Nyquist calculator! http://svi.nl/NyquistCalculator
Notes: Recommend registering with SVI for more useful info
SVI uses frequency bandwidth to calculate nyquist rate (fourier transform of psf =optical transfer function) which is smaller than ‘rule of thumb’ -> for airy1 pinhole can use sampling slightly larger than svi recommendation

## Slide 10: Image Processing
Improve the signal to noise of the image
  Background subtraction
  Filtering
Segment and measure features within the image
  Size
  Shape - Circularity/ellipticity etc.
  Intensity – per channel or ratio
  Tracking
  Changes over time
  Changes after stimulation etc.

## Slide 11: File Types
TIFF – good general choice
  Lossless storage
  Header tags for metadata
  Multipage compatible (i.e. stacks, multicolour, tile scanning etc.)
Proprietary formats (e.g. .lif) – most complete
  Lossless storage
  (Should!) Contain all metadata
  Readers required for viewing outside proprietary software
PNG – good for transfer/display
  Lossless compression
  RGB only
  No associated metadata
JPEG – ….just don’t…

## Slide 12: Image Types
2D
Hyperstacking (4,5,6,7…D)
XY
XYT
XYC
XYZ
3D
XYZT
XYZCT

## Slide 13: Histograms & Thresholds
Histogram of image shows probability density function of intensity values
  Range of intensity values determined by bit depth of image
Thresholding separates foreground (objects of interest) from background
Various algorithms available in FIJI:
  Otsu (default)
  Li
  Percentile
  …
Each will give different results
  Doesn’t really matter which one you pick!
255
0
Frequency
Intensity
Threshold

## Slide 14: Binary Images
1 bit | 21 | 2
8 bit | 28 | 256
12 bit | 212 | 4096
16 bit | 216 | 65536
Binary image formed of 0’s and 1’s – background and objects
Use threshold value calculated from histogram to determine cut-off intensity
  Otsu threshold used – threshold = 23

## Slide 15: Filtering Images
Spatial Filter:
  Image operation where each pixel value I(u,v) is changed by a function of the intensities of pixels in the neighbourhood of (u,v).
  Example: Mean filter in 3 x 3 neighbourhood
I
u
v
I(u,v)
I’
u
v
I’(u,v)
u
u+1
u-1
v
v+1
v-1

## Slide 16: Filtering Images
Applying filters:
  Raster scan processing kernel across image
1
1
1
1
1
1
1
1
1
3 x 3 Mean kernel

## Slide 17: Filtering images
No Filter
Gaussian (r=2)
Median (r=2)
Sobel Edge Detection
Notes: Although I use jpeg in this course!

## Slide 19: ImageJ/Fiji interface
File open/save
Copy/paste, invert image intensity, regions of interest
Stack operations, scale, crop, zoom, rename, LUTs
Filter, binarise, add/subtract images, subtract background
Measurement, analyse particles, intensity profiles, colocalisation
Region selection
Zoom/pan
LUTs
Downloaded plugins (many installed with Fiji)
System messages, pixel coordinates, pixel intensity

## Slide 20: Loading images
Load standard images using “Open”
  File > Open
To load image sequences
  Files ending in “0001.tif”, “0002.tif”, etc.
  File > Import > Image Sequence…
Load Leica (.lif) files using Bio-Formats
  File > Import > Bio-Formats
  Included with FIJI (download for ImageJ)

## Slide 21: Loading images
Display OME-XML metadata
  Shows formatted metadata
  Microscope and image acquisition settings (laser power, objective lens, etc.)
Use virtual stack
  Images loaded directly from storage (not loaded to RAM in advance)
  Useful for large files (>1GB)

## Slide 22: Loading images
Select relevant images
  Only shows up when >1 image stack in file

## Slide 23: Image metadata
OME-XML metadata
  Loaded via Bio-Formats
  Easier to read
Show info
  Image > Show Info…
  Plain text format
  Works for any image (content will vary)
  Shows more information than OME-XML

## Slide 24: Saving images
Save images to single .tif file
  File > Save As > Tiff…
Save image sequence
  File > Save As > Image Sequence…
  Each slice saved as a separate .tif file
  Filenames end with “0001.tif”, “0002.tif”, etc.
  Number of zeroes dictated by “Digits” option

## Slide 25: Image navigation
Move through frames using sliders
  Channel (C)
    Blue, red, etc.
  Z-slice (Z)
  Time ()
    Click  to play video
Change video speed
  Image > Stacks > Animation > Animation options
Thanks to Joe Wrennall for confocal images

## Slide 26: Worksheet – section 1
Aims
  Loading an image with BioFormats
  Selecting channels and slices with sliders
Notes
  Download “ExampleData.lif” from https://goo.gl/YrBvRU
Notes: 45 minutes
Wait 5 minutes
15:00

## Slide 27: Worksheet – section 1

## Slide 28: Image navigation
Zooming
  Select
  Left click to zoom in, right click to zoom out
  Can also zoom with up/down keys on keyboard
Dragging
  Select
  Click and hold to drag
  Position in image shown in top-left
Zoom
Drag

## Slide 29: Image navigation
Pixel coordinates
  Move the cursor over the image
  Coordinates and intensity displayed in main ImageJ/FIJI window
  If distance per pixel known, position shown in that scale, otherwise shown in pixel units
  Calibration automatically loaded if available
Manually setting distance per pixel
  Analyze > Set Scale…

## Slide 30: Brightness and contrast
Adjust how intensity is displayed
  Image > Adjust > Brightness/Contrast…
  By default 0 intensity is displayed as black and 255 (8-bit) as white
  Use min and max sliders to change display range
  Image intensity values are unchanged
Alter intensity values (optional)
  Clicking “Apply” rescales intensity values to 0-255
  Treat this function with care

## Slide 31: Lookup table (LUT)
Microscope images generally greyscale
  No colour information
  Colour determined by LUT
  Image data not altered by LUT

## Slide 32: Worksheet – section 2
Aims
  Adjusting appearance of image with Brightness/Contrast
  Changing lookup table (LUTs)
  Using zoom and pan tools
Notes: 45 minutes
Wait 5 minutes
15:00

## Slide 33: Worksheet – section 2

## Slide 34: Stack manipulation
Split channels
  Image > Color > Split channels
Merge channels
  Image > Color > Merge channels…
  Tick “create composite” to keep channels separate
Duplicate stack
  Image > Duplicate
  Can duplicate individual slices or whole stack

## Slide 35: Stack manipulation
Rename stack
  Image > Rename
Extract single slices from stack
  Image > Stacks > Tools > Make Substack…
  Enter single channel/slice numbers or ranges

## Slide 36: Intensity projections
Project stack to single plane
  Image > Stacks > Z Project…
  Max Intensity: Highlights signal
  Min intensity: Good for identifying constant background
  Also available: mean, median, sum and standard deviation
Max intensity
Min intensity
Mean intensity
Intensity standard dev.

## Slide 37: Worksheet – section 3
Aims
  Split two channels of input image
    Discard the cell image (channel 2)
  Compare approaches for extracting “good example images of nuclei”
    One image from a Z-projection
    One image from a single Z-slice
Notes: 45 minutes
Wait 5 minutes
15:00

## Slide 38: Worksheet – section 3
Substack
Max. intensity Z-projection

## Slide 39: Background subtraction
Rolling ball
  Passes a ball underneath the image
  The ball traces out features larger than its own diameter (i.e. the background)
  Repeat from opposite side to remove effect of ball radius

## Slide 40: Background subtraction
Rolling ball
  Process > Subtract Background…
  Tick “Create background” to get background image
  “Sliding paraboloid” replaces the ball with a parabola and can give better results
Rolling ball
Sliding paraboloid

## Slide 41: Image calculator
Add/subtract images
  Process > Image Calculator…
  Calculated pixel-by-pixel
  “32-bit (float) result” when negative or non-integer values may occur
Image B (background)
Image C (result)
Image A (signal)

## Slide 42: Worksheet – section 4
Aims
  Use two approaches to subtract background
    Rolling ball subtraction
    Minimum intensity projection subtraction
  Apply both subtraction methods to nuclei image from exercise 3
    Duplicate image first, then apply subtraction
    End up with two images for comparison

## Slide 43: Worksheet – section 4
Rolling ball subtraction
Minimum intensity Z-projection subtraction

## Slide 44: Selecting regions
Hand-drawing tools to select regions
  Right click for more options (red arrow)
  Can drag handles to reshape afterwards
Polygon selection
  Close loop to finish (small square)
Line tools
  Don’t need to enclose area

## Slide 45: Making measurements
Setting measurements
  Analyze > Set Measurements…
  “Redirect to” uses the regions from a binary image on a different image
Making measurements
  Analyze > Measure

## Slide 46: Linear intensity profile
Draw line on image
  Straight, freehand, segmented, etc.
Measure line profile
  Analyze > Plot Profile
  Profile displayed in new window
  “List” to get plot coordinates
  Can copy coordinates to clipboard

## Slide 47: Worksheet – section 5
Aims
  Enable specific measurements (“Area” in this case)
  Make a few measurements of a typical nucleus area

## Slide 48: Worksheet – section 5

## Slide 49: Image filtering
Apply spatial filter
  Process > Filters > [multiple]
  Sobel edge filter at Process > Find Edges
  Many require range for filtering
Custom spatial filter
  Process > Filters > Convolve…
  Specify filter kernel
Unfiltered
1px Gaussian
2px median
2px Gaussian
Edge (Sobel)
5px Gaussian

## Slide 50: Worksheet – section 6
Aims
  Test different image filters to reduce noise
  We wish to remove speckle noise whilst retaining sharp edges for nuclei

## Slide 51: Worksheet – section 6
Input image
1px median filter

## Slide 52: Intensity thresholding
Manual intensity thresholds
  Image > Adjust > Threshold…
  Set percentage above threshold
5% over threshold
15% over threshold
25% over threshold

## Slide 53: Intensity thresholding
Automatic global intensity thresholds
  Image > Adjust > Auto Threshold
  Uses a single value for the entire image
  Ability to test multiple algorithms
    http://imagej.net/Auto_Threshold
Automatic local intensity thresholds
  Image > Adjust > Auto Local Threshold
  Set size of local region

## Slide 54: Intensity thresholding

## Slide 55: Worksheet – section 7
Aims
  Test different image threshold methods to binarise image
  The main aim is to have well-defined nuclei
    A few holes in nuclei or speckles in the background aren’t a problem
  End up with black nuclei on a white background

## Slide 56: Worksheet – section 7
Input image
Huang threshold
Invert

## Slide 57: Binary operations
Make binary image
  Process > Binary > Make Binary
  Apply to intensity thresholded image
Binary operations
  Process > Binary > [multiple]
Binary options
  Process > Binary > Options
  Iterations, operation preview, etc.
Dilate
Outline
Erode
Skeletonize
Fill holes
Distance map
Unaltered

## Slide 58: Watershed segmentation
Apply binary watershed
  Process > Binary > Watershed
  Useful for splitting touching objects
  Use prior to particle analysis
  Calculates distance map, then grows points from minima until touching (object boundary)
Before watershed
25% over threshold

## Slide 59: Worksheet – section 8
Aims
  Apply binary filters to clean up image
    Remove holes in nuclei
    Split nuclei in contact
  Speckles in background still aren’t a problem
    We’ll deal with these later

## Slide 60: Worksheet – section 8
Input image
Fill holes (?)
Watershed transform

## Slide 61: Analyse particles
Run analyse particles
  Analyze > Analyze Particles…
Set limits on particles
  Size
    Image scale units if set, option for pixels
  Circularity
    Non-circular (0) or perfectly circular (1)
  Exclude on edges:
    Remove particles touching image border
Overlay (default)
Counts (“grey” LUT)
Counts (“glasbey” LUT)

## Slide 62: Worksheet – section 9
Aims
  Detect nuclei using Analyze Particles tool
  Redirect measurements to “best” nuclei image
    Analyze > Set Measurements
  Display identified objects as outlines or “count masks”

## Slide 63: Worksheet – section 9
Input image
Count masks

## Slide 64: Other useful plugins
Colocalisation (Coloc2)
  Analyze > Colocalisation > Coloc2
  Options for Pearsons (PCC), Manders (MCC) and significance testing
Stack registration (StackReg)
  Plugins > Registration > StackReg
  Aligns images in a stack to correct for sample drift
Particle tracking (TrackMate)
  Plugins > Tracking > TrackMate

## Slide 65: Macro recording
Allows short, simple bits of code to be automated
  Plugins > Macros > Record…
  Will turn each mouse click into macro code
  Create button sends code to macro editor

## Slide 66: “Batching” Macros
Process > Batch > Macro…
  Set input containing folder of images to be processed
  Set output for output images
  Either:
    Copy code from recorder
    Open saved macro

## Slide 67
Macro writing in ImageJ/Fiji
29th May 2019
CellProfiler
Summer/Autumn 2019